## Slide 1: Routing

## Slide 2: Traditional Routing
Learning switches
Link-state routing
  Dijkstra’s Algorithm
Distance-vector routing
  Bellman-Ford

## Slide 3: Basics of Routing and Forwarding

## Slide 4: Example of Network Graph
Router with 6 attached links
Router with 4 attached links

## Slide 5: A Variety of Networks
ISPs: carriers
  Backbone
  Edge (connecting to customers)
  Border (to other ISPs)
Enterprises: companies, universities
  Core
  Edge (connecting to hosts)
  Border (to outside)
Datacenters: massive collections of machines
  Aggregation and Core
  Top-of-Rack
  Border (to outside)

## Slide 6: UUNET’s North American Network
Notes: Very irregular

## Slide 7: Enterprise Network
Notes: Not very detailed, couldn’t get a better one….

## Slide 8: Partial Datacenter Network
Notes: Only a part of the network, but the takeaway is that the network is very regular, involving levels of hierarchy.

## Slide 9: Switches
Enterprise/Edge: typically 24 to 48 attached links
Aggregation switches: 192 or more
Backbone: typically fewer attached links
Border: typically very few attached links

## Slide 10: Destination-Based Routing
Paths from two different sources (to same destination) must coincide once they overlap
Notes: Why coincide?

## Slide 11: Destination-Based Routing
Paths to same destination never cross
Once paths to destination meet, they never split
Set of paths to destination create a “delivery tree”
  Must cover every node exactly once
  Spanning Tree rooted at destination
Notes: You all know what a spanning tree is?

## Slide 12: A “Delivery Tree” for a Destination

## Slide 13: Assume Destination-Based Routing
For rest of lecture (and course)…..

## Slide 14: Validity of Routing State

## Slide 15: Local and Global Routing State
Local routing state is the state in a single router
  By itself, the state in a single router can’t be evaluated
  It must be evaluated in terms of the global context
Global routing state means collection of routing state in each of the routers
  Global state determines which paths packets take
  Will discuss later where this routing state comes from

## Slide 16: “Valid” Routing State
Global routing state is “valid” if it produces forwarding decisions that always deliver packets to their destinations
  Valid is my terminology, not standard
Goal of routing protocols: compute valid state
  But how can you tell if routing state if valid?
Need a succinct correctness condition for routing
  Suggestions?
Notes: What could go wrong?

## Slide 17: Necessary and Sufficient Condition
Global routing state is valid if and only if:
  There are no dead ends (other than destination)
  There are no loops
A dead end is when there is no outgoing port
  A packet arrives, but the forwarding decision does not yield any outgoing port
A loop is when a packet cycles around the same set of nodes forever

## Slide 18: Wandering Packets
Packet reaches deadend and stops
Packet falls into loop and never reaches destination

## Slide 19: Necessary and Sufficient Condition
Global routing state is valid if and only if:
  There are no dead ends (other than destination)
  There are no loops

## Slide 20: Necessary (“only if”): Obvious
If you run into a deadend before hitting destination, you’ll never reach the destination
If you run into a loop, you’ll never reach destination
  With deterministic forwarding, once you loop, you’ll loop forever (assuming routing state is static)

## Slide 21: Sufficient (“if”): Easy
Assume no deadends, no loops
Packet must keep wandering, without repeating
  If ever enter same switch from same port, will loop
  Because forwarding decisions are deterministic
Only a finite number of possible ports for it to visit
  It cannot keep wandering forever without looping
  Must eventually hit destination
Notes: Destination is only safe deadend

## Slide 22: Checking Validity of Routing State
Focus only on a single destination
  Ignore all other routing state
Mark outgoing port with arrow
  There can only be one at each node
Eliminate all links with no arrows
Look at what’s left….

## Slide 23: Example 1

## Slide 24: Pick Destination

## Slide 25: Put Arrows on Outgoing Ports

## Slide 26: Remove Unused Links
Leaves Spanning Tree: Valid

## Slide 27: Second Example

## Slide 28: Second Example
Is this valid?

## Slide 29: Lesson….
Very easy to check validity of routing state for a particular destination
Deadends are obvious
  Node without outgoing arrow
Loops are obvious
  Disconnected from rest of graph

## Slide 30: Computing Routing State

## Slide 31: Forwarding vs Routing
Forwarding: “data plane”
  Directing a data packet to an outgoing link
  Individual router using routing state
Routing: “control plane”
  Computing paths the packets will follow
  Routers talking amongst themselves
  Jointly creating the routing state
Two very different timescales….
  Forwarding: single packet transmission times: μs
  Routing: can be seconds
  6 orders of magnitude!

## Slide 32: The “Secret” of Routing
Avoiding deadends is easy
Avoiding loops is hard
The key difference between routing protocols is how they avoid loops!
  Don’t focus on details of mechanisms
  Just ask “how are loops avoided?”
Notes: Most modern routing research is about how to make the loop-freeness a more fundamental part of the algorithm. In what I’m going to present today, it is only loop-free AFTER convergence. That’s not good enough

## Slide 33: How Can You Avoid Loops?
Easiest way: Restrict topology to spanning tree
  If the topology has no loops, packets can’t loop!
  (without making a u-turn, which can be locally prevented)

## Slide 34: Routing on Spanning Tree

## Slide 35: Easiest Way to Avoid Loops
Use a topology where loops are impossible!
Take arbitrary topology
Build spanning tree (algorithm covered later)
  Ignore all other links (as before)
Only one path to destinations on spanning trees
  So don’t have to worry about loops!

## Slide 36: Consider previous graph

## Slide 37: A Spanning Tree

## Slide 38: Another Spanning Tree

## Slide 39: Yet Another Spanning Tree

## Slide 40: Routing on a Spanning Tree
There is only one path from source to destination
How do you find that path?
Why bother? Just send packets along all paths
  No packets will loop, but some will hit deadends
  But one (and exactly one) will reach destination

## Slide 41: Flooding on a Spanning Tree
If you want to send a packet that will reach all nodes, then switches can use the following rule:
  Ignoring all ports not on spanning tree!
Originating switch sends “flood” packet out all ports
When a “flood” packet arrives on one incoming port, send it out all other ports

## Slide 42: Flooding on Spanning Tree

## Slide 43: Flooding on Spanning Tree (Again)

## Slide 44: Flooding on a Spanning Tree
This works because the lack of loops prevents the flooding from cycling back on itself
Eventually all nodes will be covered, exactly once

## Slide 45: But isn’t flooding wasteful?
Yes, but you can watch the packets going by, and learn from that
There is a single path between any two nodes
If node A sees a packet from node B come in on a particular port, what can it conclude?
It knows what port to use to reach B!

## Slide 46: Nodes can “learn” routing tables
Switch can learn how to reach nodes by remembering where flooding packets came from!
If flood packet from Node A entered switch from port 4, then switch uses port 4 to reach Node A

## Slide 47: Learning from Flood Packets
Node A
Node A can be reached
through this port
Node A can be reached
through this port
Once a node has sent a flood message, all other switches know how to reach it….
Node B

## Slide 48: Node B Responds
Node A
Node B can be reached
through this port
When a node responds, some of the switches learn where it is
Node B
Node B can be reached
through this port
Node B can be reached
through this port
Node B can be reached
through this port

## Slide 49: General Approach
Flood first packet to node you are trying to reach
All switches learn where you are
When destination responds, some switches learn where it is…
  Only some switches, because packet to you follows direct path, and is not flooded
The decision to flood or not is done on a switch-by-switch basis….

## Slide 50: Self-Learning Switch
When a packet arrives
Inspect source ID, associate with incoming port
Store mapping in the switch table
Use time-to-live field to eventually forget mapping
A
B
C
D
Packet tells switch how to reach A.

## Slide 51: Self Learning: Handling Misses
When packet arrives with unfamiliar destination
Forward packet out all other ports
Response will teach switch about that destination
A
B
C
D

## Slide 52: General Rule
When switch receives a packet:
index the switch table using destination ID
if entry found for destination {
if dest on port from which packet arrived then drop packet
else forward packet on port indicated
}
else flood
forward on all but the interface
on which the frame arrived
Why do this?

## Slide 53: Summary of Learning Approach
Avoids loop by restricting to spanning tree
This makes flooding possible
Flooding allows packet to reach destination
And in the process switches learn how to reach source of flood
No route “computation”

## Slide 54: Weaknesses of This Approach?
Requires loop-free topology (Spanning Tree)
  Must eliminate many links from physical topology
  Reducing bisection bandwidth (jargon)
  Very little control over paths (traffic engineering)
Slow to react to failures
  Tree must be recomputed
Slow to react to host movement
  Entries must time out
Spanning Trees suck (just ask an operator)

## Slide 55: On to other routing techniques…
How do we compute loop-free routes in arbitrary topologies?
Suggestions?

## Slide 56: Avoiding Loops
Central computation
  Can make sure no loops
Minimizing metric in distributed computation
  Loops are never the solution to a minimization problem
  (for well-behaved metrics)