## Slide 1: Congestion Control & TCP Refresher
Same slides, but crucial for rest of lecture

## Slide 2: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Starting sequence
number (byte offset) of data
carried in this segment
This is the number of the first byte of data in packet!

## Slide 3: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Acknowledgment gives seq # just beyond highest seq. received in order.
“What’s Next”

## Slide 4: 3-Way Handshaking
Client (initiator)
Server
SYN, SeqNum = x
SYN + ACK, SeqNum = y, Ack = x + 1
ACK, Ack = y + 1
Active Open
Passive Open
connect()
listen()
accept()

## Slide 5: Sequence Numbers
Host A
Host B
TCP Data
TCP Data
TCP
HDR
TCP
HDR
ISN (initial sequence number)
Sequence number = 1st byte
ACK sequence number = next expected byte

## Slide 6: Data and ACK in same packet
The sequence number refers to data in packet
  Packet from A carrying data to B
The ACK refers to received data in other direction
  A acking data that it received from B

## Slide 7: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Buffer space available for receiving data. Used for TCP’s sliding window.
Interpreted as offset beyond Acknowledgment field’s value.
Notes: If consume data as fast as it comes in, in sliding window this is constant.

## Slide 8: TCP Segment
IP packet
  No bigger than Maximum Transmission Unit (MTU)
  E.g., up to 1,500 bytes on an Ethernet
TCP packet
  IP packet with a TCP header and data inside
  TCP header  20 bytes long
TCP segment
  No more than Maximum Segment Size (MSS) bytes
  E.g., up to 1460 consecutive bytes from the stream
  MSS = MTU – (IP header) – (TCP header)
IP Hdr
IP Data
TCP Hdr
TCP Data (segment)

## Slide 9: Congestion Control Overview
Everything in this lecture is oversimplified.
Lots of details omitted.
But the basic points remain valid….
Notes: Deceptively complicated….

## Slide 10: Flow Control vs Congestion Control
Flow control keeps one fast sender from overwhelming a slow receiver
Congestion control keeps a set of senders from overloading the network

## Slide 11: Huge Literature on Problem
In mid-80s Jacobson “saved” the Internet with CC
One of very few net topics where theory helps; many frustrated mathematicians in networking
Less of a research focus now in the wide area
  But still actively researched in datacenter networks
  And commercial activity in wide area (e.g., Google)
…but still far from academically settled
  E.g. battle over “fairness” with Bob Briscoe…
Notes: Congestion collapse

## Slide 12: Congestion is Natural
Because Internet traffic is bursty!
If two packets arrive at the same time
  The node can only transmit one
  … and either buffers or drops the other
If many packets arrive in a short period of time
  The node cannot keep up with the arriving traffic
  … delays, and the buffer may eventually overflow

## Slide 13: Load and Delay
Average
Packet delay
Load
Typical queuing system with bursty arrivals
Must balance utilization versus delay and loss
Average
Packet loss
Load

## Slide 14: Who Takes Care of Congestion?
Network?
End hosts?
Both?

## Slide 15: Answer
End hosts adjust sending rate
Based on feedback from network
Hosts probe network to test level of congestion
  Speed up when no congestion
  Slow down when congestion

## Slide 16: Drawbacks
Suboptimal (always above or below optimal point)
Relies on end system cooperation
Messy dynamics
  All end systems adjusting at the same time
  Large, complicated dynamical system
  Miraculous it works at all!

## Slide 17: Basics of TCP Congestion Control
Congestion window (CWND)
  Maximum # of unacknowledged bytes to have in flight
  Congestion-control equivalent of receiver window
  MaxWindow = min{congestion window, receiver window}
    Typically assume receiver window much bigger than cwnd
Adapting the congestion window
  Increase upon lack of congestion: optimistic exploration
  Decrease upon detecting congestion

## Slide 18: Detecting Congestion
Network could tell source (ICMP Source Quench)
  Risky, because during times of overload the signal itself could be dropped (and add to congestion)!
Packet delays go up (knee of load-delay curve)
  Tricky: noisy signal (delay often varies considerably)
Packet loss
  Fail-safe signal that TCP already has to detect
  Complication: non-congestive loss (checksum errors)

## Slide 19: Not All Losses the Same
Duplicate ACKs: isolated loss
  Still getting ACKs
Timeout: possible disaster
  Not enough dupacks
  Must have suffered several losses

## Slide 20: How to Adjust CWND?
Consequences of over-sized window much worse than having an under-sized window
  Over-sized window: packets dropped and retransmitted
  Under-sized window: somewhat lower throughput
Approach:
  Gentle increase when uncongested (exploration)
  Rapid decrease when congested

## Slide 21: AIMD
Additive increase
  On success of last window of data, increase by one MSS
Multiplicative decrease
  On loss of packet, divide congestion window in half

## Slide 22: Leads to the TCP “Sawtooth”
t
Window
halved
Loss
Notes: Picture not realistic!!

## Slide 23: Slow-Start
In what follows refer to cwnd in units of MSS

## Slide 24: AIMD Starts Too Slowly!
t
Window
It could take a long time to get started!
Need to start with a small CWND to avoid overloading the network.

## Slide 25: “Slow Start” Phase
Start with a small congestion window
  Initially, CWND is 1 MSS
  So, initial sending rate is MSS/RTT
That could be pretty wasteful
  Might be much less than the actual bandwidth
  Linear increase takes a long time to accelerate
Slow-start phase (actually “fast start”)
  Sender starts at a slow rate (hence the name)
  … but increases exponentially until first loss
Notes: MSS vs MTU??

## Slide 26: Slow Start in Action
Double CWND per round-trip time
Simple implementation:
on each ack, CWND += MSS
D
A
D
D
A
A
D
D
Src
Dest
D
D
1
2
4
3
A
A
A
A
8

## Slide 27: Slow Start and the TCP Sawtooth
Loss
Exponential “slow start”
t
Window
Why is it called slow-start? Because TCP originally had
no congestion control mechanism. The source would just start by sending a whole window’s worth of data.

## Slide 28: This has been incredibly successful
Leads to the theoretical puzzle:
If TCP congestion control is the answer,
then what was the question?
Not about optimizing, but about robustness
  Hard to capture…

## Slide 29: Congestion Control Details

## Slide 30: Increasing CWND
Increase by MSS for every successful window
Increase a fraction of MSS per received ACK
# packets (thus ACKs) per window: CWND / MSS
Increment per ACK:
CWND += MSS / (CWND / MSS)
Termed: Congestion Avoidance
  Very gentle increase

## Slide 31: Fast Retransmission
Sender sees 3 dupACKs
Multiplicative decrease: CWND halved

## Slide 32: CWND with Fast Retransmit
segment 1
cwnd = 1
ACK 2
cwnd = 2
segment 2
segment 3
ACK 4
cwnd = 4
segment 4
segment 5
segment 6
segment 7
ACK 4
ACK 4
ACK 3
cwnd = 3
ACK 4
segment 4
3 duplicate
ACKs
cwnd = 2

## Slide 33: Loss Detected by Timeout
Sender starts a timer that runs for RTO seconds
Restart timer whenever ack for new data arrives
If timer expires:
  Set SSTHRESH  CWND / 2 (“Slow-Start Threshold”)
  Set CWND  MSS
  Retransmit first lost packet
  Execute Slow Start until CWND > SSTHRESH
  After which switch to Additive Increase

## Slide 34: Summary of Decrease
Cut CWND half on loss detected by dupacks
  “fast retransmit”
Cut CWND all the way to 1 MSS on timeout
  Set ssthresh to cwnd/2
Never drop CWND below 1 MSS

## Slide 35: Summary of Increase
“Slow-start”: increase cwnd by MSS for each ack
Leave slow-start regime when either:
  cwnd > SSThresh
  Packet drop
Enter AIMD regime
  Increase by MSS for each window’s worth of acked data

## Slide 36: Repeating Slow Start After Timeout
t
Window
Slow-start restart: Go back to CWND of 1 MSS, but take advantage of knowing the previous value of CWND.
Slow start in operation until it reaches half of previous CWND, I.e., SSTHRESH
Timeout
Fast Retransmission
SSThresh
Set to Here

## Slide 37: More Advanced Fast Restart
Set ssthresh to cwnd/2
Set cwnd to cwnd/2 + 3
  for the 3 dup acks already seen
Increment cwnd by 1 MSS for each additional duplicate ACK
After receiving new ACK, reset cwnd to ssthresh

## Slide 38: Throughput Equation
In what follows refer to cwnd in units of MSS

## Slide 39: Calculation on Simple Model
Assume loss occurs whenever cwnd reaches W
  Recovery by fast retransmit
Window: W/2, W/2+1, W/2+2, …W, W/2, …
  W/2 RTTs, then drop, then repeat
Average throughput: .75W(MSS/RTT)
  One packet dropped out of (W/2)*(3W/4)
  Packet drop rate p = (8/3) W-2
Throughput = (MSS/RTT) sqrt(3/2p)

## Slide 40: Some implications
Flows get throughput inversely proportional to RTT
  Fairness issue?
One can dispense with TCP and just match eqtn:
  Equation-based congestion control
  Measure drop percentage p, and set rate accordingly
  Useful for streaming applications

## Slide 41: How does this work at high speed?
Assume that RTT = 100ms, MSS=1500bytes
What value of p is required to go 100Gbps?
  Roughly 2 x 10-12
How long between drops?
  Roughly 16.6 hours
How much data has been sent in this time?
  Roughly 6 petabits
These are not practical numbers!

## Slide 42: Adapting TCP to High Speed
One approach: once speed is past some threshold, change equation to p-.8 rather than p-.5
We will discuss other approaches next time…

## Slide 43: Why AIMD?
In what follows refer to cwnd in units of MSS

## Slide 44: Three Congestion Control Challenges
Single flow adjusting to bottleneck bandwidth
  Without any a priori knowledge
  Could be a Gbps link; could be a modem
Single flow adjusting to variations in bandwidth
  When bandwidth decreases, must lower sending rate
  When bandwidth increases, must increase sending rate
Multiple flows sharing the bandwidth
  Must avoid overloading network
  And share bandwidth “fairly” among the flows

## Slide 45: Problem #1: Single Flow, Fixed BW
Want to get a first-order estimate of the available bandwidth
  Assume bandwidth is fixed
  Ignore presence of other flows
Want to start slow, but rapidly increase rate until packet drop occurs (“slow-start”)
Adjustment:
  cwnd initially set to 1 (MSS)
  cwnd++ upon receipt of ACK

## Slide 46: Problems with Slow-Start
Slow-start can result in many losses
  Roughly the size of cwnd ~ BW*RTT
Example:
  At some point, cwnd is enough to fill “pipe”
  After another RTT, cwnd is double its previous value
  All the excess packets are dropped!
Need a more gentle adjustment algorithm once have rough estimate of bandwidth
  Rest of design discussion focuses on this

## Slide 47: Problem #2: Single Flow, Varying BW
Want to track available bandwidth
Oscillate around its current value
If you never send more than your current rate, you won’t know if more bandwidth is available
Possible variations: (in terms of change per RTT)
Multiplicative increase or decrease:
  cwnd cwnd * / a
Additive increase or decrease:
  cwnd cwnd +- b

## Slide 48: Four alternatives
AIAD: gentle increase, gentle decrease
AIMD: gentle increase, drastic decrease
MIAD: drastic increase, gentle decrease
  too many losses: eliminate
MIMD: drastic increase and decrease
Notes: What do you think about these options?
Which one is obviously bad?
What do you think about the other ones?

## Slide 49: Problem #3: Multiple Flows
Want steady state to be “fair”
Many notions of fairness, but here just require two identical flows to end up with the same bandwidth
This eliminates MIMD and AIAD
  As we shall see…
AIMD is the only remaining solution!
  Not really, but close enough….

## Slide 50: Buffer and Window Dynamics
No congestion  x increases by one packet/RTT every RTT
Congestion  decrease x by factor 2
A
B
C = 50 pkts/RTT
x

## Slide 51: AIMD Sharing Dynamics
A
B
x1
D
E
No congestion  rate increases by one packet/RTT every RTT
Congestion  decrease rate by factor 2
Rates equalize  fair share
x2

## Slide 52: AIAD Sharing Dynamics
A
B
x1
D
E
No congestion  x increases by one packet/RTT every RTT
Congestion  decrease x by 1
x2

## Slide 53: Simple Model of Congestion Control
Two TCP connections
  Rates x1 and x2
Congestion when sum>1
Efficiency: sum near 1
Fairness: x’s converge
User 1: x1
User 2: x2
Efficiency
line
2 user example
overload
underload

## Slide 54: Example
User 1: x1
User 2: x2
fairness
line
efficiency
line
1
1
Total bandwidth 1
Inefficient: x1+x2=0.7
(0.2, 0.5)
Congested: x1+x2=1.2
(0.7, 0.5)
Efficient: x1+x2=1
Not fair
(0.7, 0.3)
Efficient: x1+x2=1
Fair
(0.5, 0.5)

## Slide 55: AIAD
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1h,x2h)
(x1h-aD,x2h-aD)
(x1h-aD+aI), x2h-aD+aI))
Increase: x + aI
Decrease: x - aD
Does not converge to fairness

## Slide 56: MIMD
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1h,x2h)
(bdx1h,bdx2h)
(bIbDx1h, bIbDx2h)
Increase: x*bI
Decrease: x*bD
Does not converge to fairness

## Slide 57: AIMD
(bDx1h+aI, bDx2h+aI)
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1h,x2h)
(bDx1h,bDx2h)
Increase: x+aD
Decrease: x*bD
Converges to fairness

## Slide 58: AIMD is only “fair” choice
But how fair is it?
Bandwidth depends on RTT
Hosts that send more flows get more bandwidth

## Slide 59: Thursday: Advanced Topics in CC